## Slide 1
<2 mm
2 mm
3 mm
4 mm
5 mm
6 mm
3 x 3
3.5 x 3.5
4 x 4
5 x 5
6 x 6
7 x 7
10 x 10
13 x 13
XGL4020/4025
40 nH – 12 µH
XGL4030
45 nH – 12 µH
XGL4040
150 nH-22 µH
XGL4012
33 nH – 1.2 µH
XGL3509/3510
90 nH
10 mm
XGL3530
100 nH – 6.8 µH
XGL3520
100 nH – 4.7 µH
XGL3515
90 nH – 2.2 µH
XGL3512
82 nH – 1.2 µH
XGL3014
82 nH – 1.8 µH
XGL7015
200 nH – 2.2 µH
XGL7030
240 nH – 18 µH
XGL1313
1.5 µH– 47 µH
XGL1010
270 nH-56 µH
XGL1060
1 µH - 10 µH
XGL5050
160 nH-33 µH
XGL5030
55 nH-22 µH
XGL5020
50 nH - 8.2 µH
XGL6030
65 nH-18 µH
XGL6020
55 nH - 10 µH
Higher Current
Smaller size and Lower Profile
Height
Footprint
XGL6060
220 nH-47 µH
XGL3020
100 nH – 4.5 µH
17 x 17 mm
XGL1712
1.0 µH – 82 µH
>10 mm
≤1 mm
XGL4015/4018
100 nH – 4.7 µH

## Slide 2: XGL - Provides all the Excellent Features of the XEL/XAL PLUS!
Lowest DCR for highest efficiency
Wider inductance range
High operating voltage (80 V, higher ratings on request)
High operating temperature range (165°C max)
Low EMI with hidden terminations
High current ratings
No thermal aging issue
AEC-Q200 qualified

## Slide 3: Highest Current and Inductance Values
XGL1010
XGL1060
XGL1313
Current
XGL1712

## Slide 4: Lowest Profile and Inductance Values
 | Height | L (µH) | 0.082 | 0.09 | 0.1 | 0.2 | 0.33 | 0.4 | 0.47 | 0.52 | 0.65 | 0.8 | 1 | 1.2 | 1.4 | 1.8
XGL3509 | 0.9 mm | DCR mΩ Isat 30% A |  | 5.9 13.9 |  |  |  |  |  |  |  |  |  |  |  | 
XGL3510 | 1.0 mm | DCR mΩ Isat 30% A |  | 4.5 14.7 |  |  |  |  |  |  |  |  |  |  |  | 
XGL3014 | 1.4 mm | DCR mΩ Isat 30% A | 2.2 16.1 |  | 2.6 13.9 | 5.0 8.7 | 7.3 7.4 |  | 9.8 6.0 |  | 13.7 5.0 | 16.1 4.5 | 19 4.1 |  | 30.6 3.3 | 38.1 3.0
XGL3512 | 1.2 mm | DCR mΩ Isat 30% A | 2.8 17.3 | 3.3 16.4 | 3.5 15.2 | 6.3 10 | 10.8 7.8 | 12.3 7.1 |  | 15.5 6.4 | 20.7 5.7 | 24.5 5.1 | 28 4.5 | 32.5 4.1 |  | 

## Slide 5: High Performance Upgrades for Popular 70xx Footprint
XGL7030
240 nH – 18 µH
XGL7015
200 nH – 2.2 µH

## Slide 6: Efficiency Advancement